## Slide 1
Similarities and differences among fifteen global water models in simulating the vertical water balance
EGU General Assembly 2020
Camelia-Eliza Telteu, Hannes Müller Schmied, Wim Thiery, Guoyong Leng, Peter Burek, Xingcai Liu, Julien Eric Stanislas Boulange, Lauren Paige Seaby, Manolis Grillakis, Yusuke Satoh, Oldrich Rakovec, Tobias Stacke, Jinfeng Chang, Niko Wanders, Fulu Tao, Ran Zhai, Harsh Lovekumar Shah, Tim Trautmann, Ganquan Mao, Aristeidis Koutroulis, Yadu Pokhrel, Luis Samaniego, Yoshihide Wada, Vimal Mishra, Junguo Liu, Simon Newland Gosling, Jacob Schewe, and Fang Zhao
© Authors. All rights reserved

## Slide 2
Review of fifteen global water models (GWMs) included in the Inter-Sectoral Impact Model Intercomparison Project phase 2b (ISIMIP2b) through a standard writing style will facilitate:
understanding the model(s);
understanding what the models have in common;
identifying what kind of data is necessary for an analysis;
to be able to select models for specific purposes.
Motivation
EGU General Assembly 2020
© Authors. All rights reserved

## Slide 3
EGU General Assembly 2020
PCR-GLOBWB
WaterGAP2
H08
VIC
MPI-HM
LPJmL
DBH
JULES-W1
CLM5.0
CLM4.5
ORCHIDEE
MATSIRO
15 Global Water Models
WAYS
mHM
CWatM
© Authors. All rights reserved

## Slide 4
Water Cycle
List with water storages and water
flows included
in GWMs
Tables with equations of water storages and water flows
How to identify similarities and differences among 15 GWMs?
Similarities and differences among
GWMs
List:
1. Canopy storage (Sc):
1.1. Inflow:
- precipitation (P)
- rainfall (Rainf)
- snowfall (Snowf)
- dewfall (D)
1.2 Outflow:
- canopy evaporation (Ec)
- throughfall (Tf)
- stemflow (Sf)
EGU General Assembly 2020
© Authors. All rights reserved
Notes: How to identify similarities and differences among 15 GWMs?
First, we created a list with water storages and water flows of the water cycle included in the models structure.
Second, we created the tables with the equations of the main water storages and flows.
Third, we find similarities and differences among GWMs.
There is a circle, iterative process: if the structure (list) is well defined, then the tables will include the right information, the equations of the water storages and fluxes, then in the end, it will be clear and easy to discover the similarities and differences between models.

## Slide 5
EGU General Assembly 2020
Preliminary results on similarities and differences among 15 GWMs
Part I
1. Interception scheme:
: H08, MPI-HM.
 f(LAI): DBH, JULES-W1, LPJmL, MATSIRO, ORCHIDEE, WaterGAP2, WAYS;
 f(LAI, SAI): CLM4.5, CLM5.0;
 f(vegetation): CWatM, VIC, PCR-GLOBWB, mHM.
2. Vegetation scheme:
 9 GWMs include PFT:
5 PFTs (JULES-W1) – 24 PFTs (CLM4.5);
 CLM5.0, ORCHIDEE, LPJmL: dynamic global vegetation model;
 WaterGAP2: LAI development model based on temperature and precipitation;
 DBH, MPI-HM, PCR-GLOBWB use prescribed vegetation;
 CWatM uses subgrid discretization;
 ORCHIDEE and LPJmL (DVPNV): CO2 fertilization effect;
 mHM: 3 major vegetation classes and long-term dynamics based on LAI.
Legend:  included and  not included in the models structure.
© Authors. All rights reserved
Notes: f(LAI): function of Leaf area index.
f(LAI, SAI): function of Leaf area index and stem area index.
f(vegetation): function of vegetation.
PFT: plant functional types system to classify plants according to their physical, phylogenetic and phenological characteristics.
Prescribed vegetation: simulated by other models and provided by ISIMIP2b framework as input or using several datasets such as Land Surface Parameter dataset 2 (MPI-HM), HYDE dataset and MIRCA, GLOBCOVER (PCR-GLOBWB).
DVPNV: dynamic vegetation composition on potential natural vegetation areas.

## Slide 6
EGU General Assembly 2020
Preliminary results on similarities and differences among 15 GWMs
Part II
3. (Potential) evapotranspiration scheme:
 Monin-Obukhov Similarity Theory: CLM4.5, CLM5.0;
 Penman-Monteith Method with or without several adjustments: CWatM, JULES-W1, MPI-HM, ORCHIDEE, WAYS;
 Priestley-Taylor Method with some adjustments: WaterGAP2, LPJmL;
 Bulk Method: H08, MATSIRO;
 Hamon Method: PCR-GLOBWB;
 Hargreaves-Samani Method: mHM.
4. Snow scheme:
 Physically based snow module: CLM4.5; CLM5.0, ORCHIDEE;
 Degree-day Method with or without several adjustments: CWatM, LPJmL, mHM, MPI-HM, PCR-GLOBWB, WaterGAP2, WAYS;
 Energy Balance Method: DBH, H08, JULES-W1, MATSIRO, VIC;
Snow layers (SL):
 14 GWMs have between 1 and 12 SLs;
 WaterGAP2 estimates snow accumulation and melt for 100 subgrid cells using a degree-day algorithm;
 JULES-W1 adapts the top soil level to represent lying snow processes.
Legend:  included in the models structure.
© Authors. All rights reserved

## Slide 7
EGU General Assembly 2020
Preliminary results on similarities and differences among 15 GWMs
Part III
5. Soil scheme:
 Number of soil layers ranges between 1 (WaterGAP2, MPI-HM) and 25 (CLM5.0).
 Total soil layer depth: generally, LSMs have a higher total soil layer depth (2 – 100 m) than GHMs (1 – 4 m).
6. Groundwater (GW) scheme:
 : DBH, mHM, MPI-HM, VIC, JULES-W1, LPJmL;
 1 GW layer: CLM4.5; 5.0; CWatM, H08, MATSIRO, ORCHIDEE, PCR-GLOBWB, WaterGAP2, WAYS;
 H08: 1 renewable and 1 nonrenewable GW layer;
 MATSIRO: dynamic groundwater scheme and has 13 GW layers.
Legend:  included and  not included in the models structure.
© Authors. All rights reserved

## Slide 8
We needed a good list of the water storages and water flows included in the models.
We needed clear and relevant definitions of the variables used by the models.
We created rules for the standard writing style of the GWMs.
This study is useful for a better understanding of how 15 GWMs work.
This study is useful for further model (inter)comparison.
Outlook: to identify similarities and differences among 15 GWMs regarding their parameters, used for calibration, and variables included in their equations.
CONCLUSIONS
EGU General Assembly 2020
© Authors. All rights reserved