## Slide 1: IAM investment response to biophysical climate impacts on water, energy and land in SDGs and climate policies
Adriano Vinca, Muhammad Awais, Edward Byers, Oliver Fricko, Volker Krey, Keywan Riahi
International Institute for Applied Systems Analysis (IIASA)
Sixteenth IAMC Annual Meeting 2023
Venice, Italy, 15 November 2023

## Slide 2: Former investment assessments using IAMs do not include climate impacts
Kulkarni et al., 2022. PLOS Sustain Transform
Now several IAMs are detailed enough to include some biophysical climate impacts and assess climate uncertainty on investments
Notes: Adaptation is from: Schinko et al. [41] Global costs of building dikes in adaptation to sea-level rise

## Slide 3: Approach: MESSAGEix-GLOBIOM IAM
Climate policy
2.6 W/m2 target
Climate impacts
RCP 2.6, 6.0
Hydrology: Precipitation pattern/runoff, groundwater intensity
Desalination potential
Crop Yield changes
Renewable energy
Cooling/heating demand
Thermal power plant cooling capacity
Based on: ISIMIP 2b (Frieler et al. 2017 ),Byers et al., 2018, Gernaat et al., 2021 etc.)
SDG measures
Food Heathy (EAT-Lancet) diet, reduce food waste
Water Efficiency improvements, environmental flow
constraints, piped water access, wastewater
treatment
Energy Maximized electrification, phase-out traditional bio, cooling gap
Life on land Protected natural land (>30%)
Based on: Doelman et al. 2022, MESSAGE-ACCESS, Van Vuuren et al., 2019, Parkinson et al., 2019, Frank et al., 2021, Hasegawa et al., 2015, Pastor et al., 2019

## Slide 4
Scenario | Climate Forcing (W/m2) | SDGs | Impacts | Water supply reliability
SSP2-noCF | 6.0 | No additional effort | Frozen to 2020 | Low-Med-High*
SSP2-CF | 6.0 | No additional effort |  | Low-Med-High
SSP2-SDG-noCF | 6.0 |  | Frozen to 2020 | Low-Med-High
SSP2-SDG-CF | 6.0 |  |  | Low-Med-High
SSP2-26-SDG-CF | 2.6 |  |  | Low-Med-High
SSP2-26-CF | 2.6 | No additional effort |  | Low-Med-High
SSP2 – Middle of the Road Socio Economic Pathway
CF – Climate Feedback
* Low = average values of multi-annual monthly distribution
Med = 70th percentile
High = 90th percentile
Notes: Radiative forcing (or climate forcing[1]) is the change in energy flux in the atmosphere caused by natural or anthropogenic factors of climate change as measured by watts / metre

## Slide 5: Energy supply and water infrastructure investments to achieve WEL SDGs
SDG 2,15: Clear benefits in energy and water investments. Less agriculture demand
SDG6: long-term higher costs than short term
Limitation: SDG7*
Energy access & clean cooking demand–side costs not taken into account. Soft-link to MESSAGE-Access-E-use
Literature estimates
Our results
Notes: This is the sum of the difference for all regions
Focus on wel range and reliability
Explore regional differentiation
Figure with the effect of diff SDG on water costs

## Slide 6: Water investments breakdown
Cost increase to meet WEL SDGs
World: +12%
South Asia: +30%
How much does it vary when including climate impacts?
Climate
Uncertainty
?
Notes: What are the sectoral increase in SDG6 and reduction in SDG2,15

## Slide 7: Cost changes in the Energy supply and water infrastructure to meet WEL SDGs
Regions with high water cost increase also have the highest climate change uncertainty, and the lowest adaptive capacity
Climate
Uncertainty
Notes: Why FSU high long term water cost?

## Slide 8: Cost changes in the Energy supply and water infrastructure to meet WEL SDGs
Energy:
Sub-Saharan Africa and South Asia have high energy investment increase
Regions with high water cost increase also have the highest climate change uncertainty, and the lowest adaptive capacity
Notes: Why FSU high long term water cost?

## Slide 9: Cost changes in the Energy supply and water infrastructure to meet WEL SDGs
Temporal dimension:
long-term cost of maintaining the SDG targets is often higher and more uncertain than reaching the targets.
Energy:
Sub-Saharan Africa and South Asia have high energy investment increase
Regions with high water cost increase also have the highest climate change uncertainty, and the lowest adaptive capacity
Notes: Why FSU high long term water cost?

## Slide 10: Climate impacts and mitigation scenarios

## Slide 11: Climate mitigation Energy Supply investments
Results fall in the lower range of previous estimates.
Energy supply mitigation inv and O&M affected by max 20% by climate impacts.
Scenarios to limit temp. increase to 2DC
Impacts on energy in MESSAGEix-Nexus:
Capacity factor of thermal power plants (low share in mitigation)
Hydropower potential
Electricity for water
Cooling gap, not changing in our sensitivity

## Slide 12: Conclusions
Limitations:
Land cost assessment
Model intercomparison complicated due to model differences
Supply vs demand detail
Climate impacts included: no floods and droughts
Model temporal resolution
Limited to two RCP climate scenarios
Insights:
SDG costs might vary up to 30pp because of climate change in the most stressed regions
Maintaining long-term SDG targets might be more costly than reaching them, and highly impacted by climate
Land SDG benefits for WE investments
Recommendations and way forward
Coordinate among land IAM modellers to include investments in their outputs
Improve demand side investment assessment in MESSAGEix
Sensitivity on land-use models to improve robusteness of the results
Solutions to represent seasonal impacts or higher temporal resolution
Cover a continuous space of climate scenarios

## Slide 13: IAM investment response to biophysical climate impacts on water, energy and land in SDGs and climate policies
Thank you!
Contact: Adriano Vinca
vinca@iiasa.ac.at
Sixteenth IAMC Annual Meeting 2023
Venice, Italy, 15 November 2023

## Slide 14: Back-up

## Slide 15: MESSAGEix-GLOBIOM-Nexus
air pollution emission
Population
Economy
G4M
spatially explicit forest management model
GLOBIOM
integrated agricultural, bioenergy and forestry model
MESSAGEix
comprehensive energy system representation, covering all GHGs, integration across different modules
socio-economic drivers
consistency of land-cover changes (spatially explicit maps of agricultural, urban, and forest land)
carbon and biomass price
agricultural and forest bioenergy potentials, land-use emissions and mitigation potential
National level Projections
MAGICC
simple climate model
GAINS
GHG and air pollution mitigation model
GHG and aerosol emissions
demand
response
iteration
MACRO
Aggregated macro-economic model
service
prices
socio-
economic
drivers
EPIC
agricultural crop model
Buildings
buildings stock, appliances, energy access
Materials production and recycling of key materials
Transport vehicle stock, modal split,
cost and value of time
energy structure
CWatM
global hydrological model
water availability
Nexus Water and agriculture
+ water requirements
Limitation: GLOBIOM does not provide investment assessment of land-related infrastructure or practices

## Slide 16: South Asia, India. Investments to meet WEL SDGs
Variability in water extraction (pumping gw, desalinating, treating). Small variations in fossil and renewable electricity generation investments

## Slide 17: Limited intra-regional variability on mitigation costs
Impacts on energy in MESSAGEix-Nexus:
Capacity factor of thermal power plants (low share in mitigation)
Hydropower potential
Electricity for water
Cooling gap, not changing in our sensitivity

## Slide 18: Water and Energy supply investment requirements with SDGs 7*

## Slide 19: Water and Energy supply investment requirements with SDGs 6
Notes: Why FSU increase inv in energy for SDG6?

## Slide 20: Water and Energy supply investment requirements with SDGs 2 and 15
Notes: Why China had energy cost increase?

## Slide 21: Timeseries and model comparison

## Slide 22: Timeseries and model comparison

## Slide 23: Climate impacts on business as usual

## Slide 24: Climate impacts on yield
Similarities with IMAGE: Middle east yield increase, pacific asia yield losses. Higher changes in MESSAGE-GLOBIOM

## Slide 25: 2.6 impacts: crop production
Land impacts still play a role, but not as much as in 6p0. The range was +- 50%

## Slide 26: Decompose investment by 3 impacts
Biggest contribution is the land impact (GLOBIOM)
Cooling gap impact mostly affect Middle east and Central Asia
Greatest water inv reduction in South Asia (90%). Related to huge agriculture production loss

## Slide 27: Land costs assessment: not investments
Afforestation = missed revenue from timber production (timber price – timber harvest cost) * forest land diff
Fertilizer use Fertilizer cost * fertilizer consumption
Irrigation (no info on the technologies) average irrigation cost(r,y) * irrigated land
Crop production cost Production cost(cr) * production

## Slide 28: Renewable water availability

## Slide 29: Power plant cooling
Small %

## Slide 30: v
Most significant change in is the water withdrawals for irrigation as adaptation strategy

## Slide 31: Crop production and land
Very different sensitivity across the two models

## Slide 32: Fertilizer use
Important role of fertilizers in changing yields in the land sectors.
NH3 nexus GLOBIOM-MESSAGE could be explicitly represented, in order to take into account energy needs