## Slide 1
Scaling near-term climate benefits through low-GWP refrigerants and energy efficiency in China
Pengnan Jiang1, 2,* | Peking University / IIASA
Pallav Purohit2, Xueying Xiang3, Ziwei Chen1, Fuli Bai1, Xingchen Zhao1, Xu Zhang1, Jianxin Hu1,*
1 College of Environmental Sciences and Engineering, Peking University, Beijing, 100871, China
2 Pollution Management Research Group, Energy, Climate, and Environment (ECE) Program, International Institute for Applied Systems Analysis (IIASA), Laxenburg, A-2361, Austria
3 Department of Civil and Environmental Engineering, National University of Singapore, 119077, Singapore
NCGG in Utrecht
15 June 2026

## Slide 2
Background: cooling is a policy target and a near-term climate risk
2
This motivates a China-focused, sector-specific assessment that connects refrigerant transition, efficiency, emissions, and climate response.
Global Cooling Pledge
-68%
cooling emissions by 2050 vs. 2022
+50%
average efficiency of new air conditioners by 2030
Policy benchmark: refrigerants + efficiency + access
WMO ozone assessment
Kigali
No controls
Kigali pathway lowers projected HFC emissions, forcing, and warming.
China's manufacturing centrality
81.2%
of 2021 global HFC production in CO₂-eq
81.0%
of world RAC output 56% domestic / 44% export
RAC refrigerant transition
2024 RAC shipments in workbook: 202 million units; R-32 share: 77%.
Sources: UNEP/Cool Coalition; WMO Ozone Assessment; China IOL; 2021 global F-gas workbook.

## Slide 3
Model boundary: four cooling sectors
3
The model focuses on four major cooling sectors; other F-gas uses remain outside the quantified boundary.
RAC
Room AC
split/window room AC;
household heat-pump cooling
HCFC-22 / HFC-410A
→ HFC-32 / HC-290
MAC
Mobile AC
passenger cars, buses,
trucks and EV AC
HFC-134a
→ HFO-1234yf / CO₂
CAC
Commercial AC
unitary, VRF,
chillers and heat pumps
HCFC-22 / HFC-410A / HFC-134a
→ HFC-32 / HFOs / natural refrigerants
CCR
Cold chain
display cabinets, cold rooms,
transport refrigeration
HFC-404A / HFC-507A / HFC-134a
→ HC-290 / CO₂ / ammonia
Each sector is modeled separately because equipment lifetimes, refrigerant choices, efficiency pathways, and costs differ.
Sources: sector boundary adapted from this study, XMind classification, and TEAP/RTOC sector taxonomy.

## Slide 4
Research question and scenarios
4
Research gap
Cooling demand, HFC controls, efficiency standards, power-sector CO₂, air pollutants, and climate response are often assessed separately.
Question
What climate and air-quality improvement could China achieve by considering low-GWP refrigerants and higher efficiency together?
Scenario design
BAU
recent market refrigerants + current efficiency
KAE
Kigali-compliant HFC phase-down + China efficiency plan
ATE
faster low-GWP transition + stronger efficiency gains
BAU = Business as usual; KAE = Kigali Amendment + Efficiency; ATE = Accelerated Transition + Efficiency.
All scenarios use the same 2022-2060 demand pathway; mitigation comes from refrigerants and efficiency, not reduced cooling service.
Sources: Kigali Amendment; Global Cooling Pledge; China efficiency-policy assumptions in this study.

## Slide 5
Technical route: RAC-DEC integrates demand, emissions, climate, and cost
5
A bottom-up chain converts sector activity into HFCs, electricity, RF / warming, and costs.
1
Demand drivers
population, income,
CDD, floor area,
vehicles, cold chain
>
2
Stock turnover
sales, in-use stock,
retirements,
Weibull lifetime
>
3
HFC bank-flow
mix, charge,
operation, service,
end-of-life leakage
>
4
Energy pathway
efficiency, hours,
electricity, CO₂,
SO₂ / NOₓ / PM₂.₅
>
5
Climate & cost
HFC IRF metrics,
CO₂ TCRE,
CAAC and MAC
RAC
room AC
MAC
vehicle AC
CAC
comm. AC
CCR
cold chain
Uncertainty
Direct HFC Monte Carlo: activity +/-5%, emission factors +/-10%, WPP population range. Indirect emissions and climate response carry added sensitivity bands.
Annual model years: 2000-2060; mitigation summaries use 2022-2060 cumulative reductions and 2060 climate response.
Source: RAC-DEC model and methods in this study / SI.

## Slide 6
Demand result: equipment stock growth sets the scale of mitigation
6
By 2060, stock roughly doubles; the 2022 mix shows the starting structure for new equipment growth.
Sources: model results; IEA/OWID; Wang et al.; CLASP/Mepsy; sector workbooks.

## Slide 7
Low-GWP refrigerants drive the largest HFC consumption cut
7
Historical context and mitigation scenarios
Scenario means and shaded bands show model uncertainty.
12.6 ± 0.4 Gt
cumulative HFC consumption reduction, 2022-2060
~70%
of the HFC consumption cut comes from Kigali-compliant controls
Sources: model results in this study; Bai et al.; Ozone Secretariat inventory context.

## Slide 8
Direct HFC emissions
8
Shaded bands
show Monte Carlo uncertainty around each scenario pathway
Bank lag
existing equipment stocks delay the emissions response after consumption changes
ATE declines faster; BAU emissions persist through 2060.
Source: direct-HFC bank-flow model and Monte Carlo uncertainty in this study.

## Slide 9
Updated accounting connects annual emissions to cumulative mitigation
9
Total GHG combines direct HFC emissions and indirect CO₂; bars report direct-HFC, indirect-CO₂, and total-GHG reductions.
Source: updated total-GHG accounting in this study; indirect CO₂ from electricity-demand module.

## Slide 10
Co-benefits: efficiency cuts pollutants while RF and warming fall
10
Air-quality gains
1.82 Mt
avoided SO2, 2022-2060
3.65 Mt
avoided NOx, 2022-2060
0.31 Mt
avoided PM2.5, 2022-2060
2060 ATE vs BAU: RF ↓0.0345 ± 0.0049 W m-2; warming ↓0.0154 ± 0.0130 °C.
Sources: model results; RF/temperature response calculation; corrected power-sector pollutant factors.

## Slide 11
Provincial emissions maps: demand concentration becomes climate exposure
11
Maps show stock/activity-weighted proxy allocations of direct HFC plus indirect CO₂ emissions and ATE avoided emissions.
Source: provincial proxy allocation and emission model results in this study.

## Slide 12
Preliminary sector net-cost screening
12
Preliminary screening: RAC/MAC use LCC/workbooks; CAC/CCR include refrigerant proxy + electricity savings; retrofit CAPEX/OPEX not fully parameterized.

## Slide 13
Preliminary annual marginal abatement cost curves
13
Preliminary screening: RAC/MAC use LCC/workbooks; CAC/CCR include refrigerant proxy + electricity savings; retrofit CAPEX/OPEX not fully parameterized.

## Slide 14
Take-home: mitigation scale, policy bridge, and PFAS question
14
China matters globally
81.2% of 2021 global HFC production (CO₂-eq) and ~70% of world RAC output: China shapes both demand and supply chains.
Mitigation scale is large
ATE cuts HFC consumption by 12.6 ± 0.4 Gt CO₂-eq and total GHG by 14.5 Gt CO₂-eq during 2022–2060.
Efficiency makes it energy policy
Electricity savings reach ~19,600 TWh and avoid 4.1 Gt indirect CO₂: about 220× Three Gorges annual output, or 1.9× China 2025 power use.
A governance bridge
Montreal/Kigali controls substances; UNFCCC/NDCs target emissions. Cooling policy can connect refrigerants, efficiency, and power-sector CO₂.
Open question for the next transition: How can low-GWP refrigerants deliver climate benefits without creating tomorrow's PFAS/TFA legacy?
Scale context: Three Gorges designed annual generation = 88.2 TWh; China 2025 electricity use = 10.4 PWh. Electricity savings are modelled ATE vs BAU cumulative savings.
Sources: model results; China IOL; Three Gorges design output; China electricity statistics.

## Slide 15
Thank you
Questions and discussion
Pengnan Jiang | Peking University / IIASA
pnjiang@pku.edu.cn; jiangp@iiasa.ac.at